LZ77 Compression
- We wanted to do LZ77
- Sliding Window
- Inefficient, requires large memory
- Turns out LZ77 performs poorly for typical sensor network data
	LZ77	RLE	Huffman
Volcano	99.7%	100.1%	81.6%
SHIMMER	88.5% - 98.8%	100.1%	70.8%
Marmot chirps	98.5%	100.2%	70.2%

---
Variable Block Size Delta Encoding
- We found that delta encoding yielded good compression ratios.
- Fixed size packets (30 – 100 bytes)
- We encode deltas in the fewest bits possible
- Each packet has a header
  - First data element
  - Block size
  - Bits per delta
  - 3 bytes for SHIMMER data

---
- At each time step we calculate the delta
- We find the # of bits needed to encode the delta
- Each delta is encoded with the bits needed for the largest delta
- New elements arrive
- See if the new delta fits
- Send block and start over

---
- Minimal computation
- Yields good compression ratios for sensor data
- High variability reduces compression
	Delta encoding	LZ77	RLE	Huffman
Volcano	53.3%	99.7%	100.1%	81.6%
SHIMMER	42.2% - 62.8%	88.5% - 98.8%	100.1%	70.8%
Marmot Chirps	33.1%	98.5%	100.2%	70.2%

---
Demo