Compression for Wireless Sensor Networks
Daniel Shteremberg and Jason Waterman
Harvard
School of Engineering
and Applied Sciences

---
Sensor Networks: Coping with Limited Resources
Sensor nodes are severely resource constrained
  - 8 MHz CPU
  - 10 KB of memory
  - ~100 Kbps of radio link bandwidth (best case)
  - 200 mAh to 2000 mAh batteries
Radio is by far the biggest drain on energy
  - ~19 ma to send and receive
  - Sending a byte is the equivalent of executing hundreds of instructions
Compression could be a big win
  - If it can be made to work under the resource constraints
Data

---
Data Sources

---
Data Sources
Seismic data collected at 100 Hz, 24 bit resolution

---
Data Sources
Acoustic marmot data
  - Very high data rate 24K Hz, 16 bit

---
Data Sources

---
Data Sources
3 axis accelerometer data, 3 axis gyroscope data
  - 100 Hz, 12 bit

---
LZ77 Compression
We wanted to do LZ77
  - Sliding Window
  - Inefficient, requires large memory
  - Turns out LZ77 performs poorly for typical sensor network data

---
Variable Block Size Delta Encoding
At each time step we calculate the delta
We find the # of bits needed to encode the delta
Each delta is encoded with the bits needed for the largest delta
New elements arrive
See if the new delta fits
Send block and start over

---
Variable Block Size Delta Encoding
Minimal computation
Yields good compression ratios for sensor data
High variability reduces compression

---
Conclusions and Future Work